## Slide 1: Computer codes the representation of all numeric data and non-numeric data in binary digits is known as computer codes. The computer code is represented in different coding schemes.

## Slide 2: DIGITAL CODES
In practice the digital electronics requires to handle data which may be numeric, alphabets and special characters. This requires the conversion of the incoming data into binary format before it can be processed. There is various possible ways of doing this and this process is called encoding. To achieve the reverse of it, we use decoders.

## Slide 3
Encoding: is the process of putting a sequence of characters (letters, numbers, punctuation, and certain symbols) into a specialized format for efficient transmission or storage.
Decoding: is the opposite process -- the conversion of an encoded format back into the original sequence of characters.

## Slide 4
WEIGHTED AND NON-WEIGHTED CODES:- There are two types of binary codes
1) Weighted binary codes
2) Non- weighted binary codes
In weighted codes, for each position ( or bit) ,there is specific weight attached. For example, in binary number, each bit is assigned particular weight 2n where ‘n’ is the bit number for n = 0,1,2,3,4 the weights are 1,2,4,8,16 respectively. Example :- BCD
Non-weighted codes are codes which are not assigned with any weight to each digit position, i.e., each digit position within the number is not assigned fixed value. Example:- Excess – 3 (XS -3) code and Gray codes .

## Slide 5: BINARY CODE
The binary number system has many advantages and is widely used in digital systems. However, there are times when binary numbers are not appropriate. Since we think much more readily in terms of decimal numbers than binary numbers, facilities are usually provided so that data can be entered into the system in decimal form, the conversion to binary being performed automatically inside the system. In fact, many computers have been designed which work entirely with decimal numbers. For this to be possible, a scheme for representing each of the 10 decimal digits as a sequence of binary digits must be used.

## Slide 6: Coding schemes:
Some important coding schemes are as follows:
1) BCD (Binary Coded Decimal)
2) ASCII (American Standard Coded Decimal Interchange Code)
3) ESCDIC (Extended Binary Coded Decimal Interchange Code)
4) Unicode

## Slide 7: Alternate Forms of Binary Representations
There are many different ways to represent binary numbers, other than the 4 representation that we have discussed.
Many of these alternate representations are used to support specific applications and requirements, for example:
(01) A telephone keypad having the digits 0 to 9 generates BCD codes for the keys pressed.
(02) Most digital systems display 9-segment LED display panels, also used BCD Code to display the decimal numbers.

## Slide 8: BCD Code:
It is used to represent decimal digit in binary.
It is a 4-bit code.
It means decimal digit is represented by 4 binary digits.
Used in early computer.
The BCD Code representing decimal digits 0 to 9.

## Slide 9
Decimal | BCD | Decimal | BCD
0 | 0000 | 5 | 0101
1 | 0001 | 6 | 0110
2 | 0010 | 7 | 0111
3 | 0011 | 8 | 1000
4 | 0100 | 9 | 1001
Example: convert decimal 425 to BCD.
4 = 0100
2 = 0001
5 = 0101

## Slide 10: The Weighted Codes
(A) The BCD Code
Binary Coded Decimal (BCD) code is a 4-bit binary code for each decimal digit in a number.
A number with k decimal digits will require 4k bits in BCD.
No need to perform arithmetic operations to convert decimal numbers into BCD code.
Decimal | BCD Code | Decimal | BCD Code
0 | 0000 | 5 | 0101
1 | 0001 | 6 | 0110
2 | 0010 | 7 | 0111
3 | 0011 | 8 | 1000
4 | 0100 | 9 | 1001

## Slide 11: BCD Code
The first 10 combinations represent the decimal digits 0 to 9 and the remaining six 4-bit combinations 1010, 1011, 1100, 1101, 1110 and 1111 are considered to be invalid and do not exist.
Examples:
  45 decimal number is equivalent in BCD 0100 0101.
  2067 decimal number = 0010 0000 0110 0111 in BCD
BCD Addition:
  Multi-digit BCD numbers can be added together.
  23 0010 0011
  + 45 0100 0101
  68 0110 1000

## Slide 12
Consider the next example where the least significant numbers add up to a number greater than 9 for which there is no valid BCD code
23 0010 0011
+ 48 0100 1000
71 0110 1011
In such cases, add 0110 (6) in invalid BCD code, if a carry results, it is added to the next most significant digit. Thus
23 0010 0011
+ 48 0100 1000
1
0110 1011
+ 0110
71 <-> 0111 0001

## Slide 13: Gray Code (non-wieghted code)
The Gray code does not have any weights assigned to its bit positions (non-positional code).
The Gray code is different from the unsigned binary code as successive values of Gray code differ by only one bit.
The bits in Red change in successive values of Gray code representation.
Decimal | Binary | Gray Code | Decimal | Binary | Gray Code
0 | 0000 | 0000 | 5 | 0101 | 0111
1 | 0001 | 0001 | 6 | 0110 | 0101
2 | 0010 | 0011 | 7 | 0111 | 0100
3 | 0011 | 0010 | 8 | 1000 | 1100
4 | 0100 | 0110 | 9 | 1001 | 1101

## Slide 14: Alphanumeric Codes
Besides numbers, we have to represent other types of information
  letters of alphabet, mathematical symbols.
For English, alphanumeric character set includes
  10 decimal digits
  26 letters of the English alphabet (both lowercase and uppercase)
  several special characters
We need an alphanumeric code
  ASCII
  American Standard Code for Information Exchange
  Uses 7 bits to encode 128 characters

## Slide 15: ASCII Code
7 bits of ASCII Code
  (b6 b5 b4 b3 b2 b1 b0)2
Examples:
  A  65 = (1000001),…, Z  90 = (1011010)
  a  97 = (1100001), …, z  122 = (1111010)
  0 48 = (0110000), …,9  57 = (0111001)
128 different characters
  26 + 26 + 10 = 62 (letters and decimal digits)
  32 special printable characters %, *, $
  34 special control characters (non-printable): BS, CR, etc.

## Slide 16: Representing ASCII Code
7-bit
Most computers manipulate 8-bit quantity as a single unit (byte)
  One ASCII character is stored using a byte
  One unused bit can be used for other purposes such as representing Greek alphabet, italic type font, etc.
The eighth bit can be used for error-detection
  parity of seven bits of ASCII code is prefixed as a bit to the ASCII code.
  A  (0 1000001) even parity
  A  (1 1000001) odd parity
  Detects one, three, and any odd number of bit errors

## Slide 17: ASCII Code:
It was published in 1968 by ANSI ( American national standard institute) .
Used is personal computer
The 7-bit code can represent 128 characters.
This 7 bit code is not enough to represent some graphical character on computer screen.
8 bit code can represent 256 characters.
8 bit code can represent graphical characters.

## Slide 18
Char | Dec | Binary | Char | Dec | Binary | Char | Dec | Binary
! | 033 | 00100001 | A | 065 | 01000001 | a | 097 | 01100001
" | 034 | 00100010 | B | 066 | 01000010 | b | 098 | 01100010
# | 035 | 00100011 | C | 067 | 01000011 | c | 099 | 01100011
$ | 036 | 00100100 | D | 068 | 01000100 | d | 100 | 01100100
% | 037 | 00100101 | E | 069 | 01000101 | e | 101 | 01100101
& | 038 | 00100110 | F | 070 | 01000110 | f | 102 | 01100110

## Slide 19
' | 039 | 00100111 | G | 071 | 01000111 | g | 103 | 01100111
( | 040 | 00101000 | H | 072 | 01001000 | h | 104 | 01101000
) | 041 | 00101001 | I | 073 | 01001001 | i | 105 | 01101001
* | 042 | 00101010 | J | 074 | 01001010 | j | 106 | 01101010
+ | 043 | 00101011 | K | 075 | 01001011 | k | 107 | 01101011
, | 044 | 00101100 | L | 076 | 01001100 | l | 108 | 01101100
- | 045 | 00101101 | M | 077 | 01001101 | m | 109 | 01101101
. | 046 | 00101110 | N | 078 | 01001110 | n | 110 | 01101110
/ | 047 | 00101111 | O | 079 | 01001111 | o | 111 | 01101111

## Slide 20
0 | 048 | 00110000 | P | 080 | 01010000 | p | 112 | 01110000
1 | 049 | 00110001 | Q | 081 | 01010001 | q | 113 | 01110001
2 | 050 | 00110010 | R | 082 | 01010010 | r | 114 | 01110010
3 | 051 | 00110011 | S | 083 | 01010011 | s | 115 | 01110011
4 | 052 | 00110100 | T | 084 | 01010100 | t | 116 | 01110100
5 | 053 | 00110101 | U | 085 | 01010101 | u | 117 | 01110101
6 | 054 | 00110110 | V | 086 | 01010110 | v | 118 | 01110110
7 | 055 | 00110111 | W | 087 | 01010111 | w | 119 | 01110111
8 | 056 | 00111000 | X | 088 | 01011000 | x | 120 | 01111000
9 | 057 | 00111001 | Y | 089 | 01011001 | y | 121 | 01111001
: | 058 | 00111010 | Z | 090 | 01011010 | z | 122 | 01111010

## Slide 21
; | 059 | 00111011 | [ | 091 | 01011011 | { | 123 | 01111011
< | 060 | 00111100 | \ | 092 | 01011100 | ¦ | 124 | 01111100
= | 061 | 00111101 | ] | 093 | 01011101 | } | 125 | 01111101
> | 062 | 00111110 | ^ | 094 | 01011110 | ~ | 126 | 01111110
? | 063 | 00111111 | _ | 095 | 01011111 | _ | 127 | 01111111
@ | 064 | 01000000 | ` | 096 | 01100000 |  |  | 

## Slide 22: EBCDIC Code:
It is 8 bit code.
It is divided in two groups of 4 bits.
Each group ca represent one hexadecimal digit.
Used in mainframe computer.
It can represent 256 character.
EBCDID developed by IBM.
Normally used in mainframe computer.
It can represent 256 character.

## Slide 23: Unicode :
It is 16 bit code.
It can represent 65536 characters.
It has started to replace ASCII Code.
It can represent the characters of all languages in the word.